## Slide 1: Boolean Algebra

## Slide 2: Circuit Simplification Using Boolean Algebra
The algebraic method used to simplify digital circuits applies a number of Boolean laws to successively simplify complex equations. Selected laws and rules are applied, step by step, to the original equation, so as to eventually arrive at a simplified version that can be implemented with a smaller number of gates and therefore lead to a simpler circuit.

## Slide 3: Boolean Laws
The laws of Boolean algebra are similar in some ways to those of standard algebra, but in some cases Boolean laws are unique. This is because when logic is applied to digital circuits, any variable such as A can only have two values 1 or 0, whereas in standard algebra A can have many values

## Slide 4: Associative Law
The order of calculation can be changed without affecting the result (Change which terms are in brackets, or remove brackets). Note: This is only OK so long as all signs (+ or •) are the same.
2a. Boolean addition (OR): (A+B)+C = A+(B+C) = A+B+C
2b. Boolean Multiplication (AND): (A•B)•C = A•(B•C) = A•B•C = ABC

## Slide 5: Commutative Laws
In a group of variables connected by operators AND or OR, the order of the variables does not matter.
1a. Boolean addition (OR): A+B = B+A
1b. Boolean multiplication (AND): A•B = B•A

## Slide 6: Distributive Laws
The same answer is arrived at when multiplying (ANDing) a variable by a group of bracketed variables added (ORed) together, as when each multiplication (AND) is performed separately.
Law 3a is similar to factoring in normal algebra, but law 3b is unique to Boolean algebra because unlike normal algebra, where A x A=A2, in Boolean algebra A•A = A
3a. A•(B+C) = A•B+A•C
3b. A+(B•C) = (A+B) • (A+C)